## Slide 1: MSRC분석
김서진

## Slide 2: Don’t Let RAID Raid the Lifetime of your SSD Array
Sangwhan Moon, HotStorage13

## Slide 3: Protection scheme to improve the reliability of SSD
  Error Correcting Code(ECC)
  Flash Translation Layer
    Log-like Writing and Garbage Collection
    Wear-leveling
  System Level Protection Scheme
    -Parity Protection(RAID5)
    : require additional writes -> endurance problem of SSD

## Slide 4: About RAID5
Minimum number of disks: 3
Minimum number of volume : (n-1) x volume per 1 disk
Description: all data and parity are distributed to all disks, but not evenly distributed.
Parity protection
  -

## Slide 5: Parity Protection
Def. Protect a device array from a device failure
  - Protect each page group from a page error
Parity = XOR of ALL data
  Parity update results in additional writes

## Slide 6: Parity protection
Parity update -> additional write
  For a small write , Write amplification:2
  For a large write, write amplification: N/(N-1)
  (N is the number of SSDs in RAID)

## Slide 7: Parity protection
2. Parity increase space utilization
- less efficient garbage collection
- more write amplification
decrease the lifetime of SSDs

## Slide 8: Lifetime model

## Slide 9: Markov model
Analyze single SSD’s reliability and device level protection
Page Error Rate Model at x write count
  Bit errors accumulate until access time
  ECC detects / corrects the bit error

## Slide 10: 논문 page
1~2p
RAID5 backgrounds