## Slide 1: [171212]논문스터디
김서진

## Slide 2: Don’t let RAID Raid the lifetime of your SSD Array (HotStorage’13)
Motivation
  - RAID5 could be less endurable because of parity protection.
Solution
  - Analytical model show that RAID5 is less reliable than RAID0 with a small number of devices because of write amplification
Evaluation

## Slide 3: Parity Protection
Def. Protect a device array from a device failure
  - Protect each page group from a page error
Parity = XOR of ALL data
  Parity update results in additional writes

## Slide 4: Parity protection
Parity update -> additional write
  For a small write , Write amplification:2
  For a large write, write amplification: N/(N-1)
  (N is the number of SSDs in RAID)

## Slide 5: Parity protection
2. Parity increase space utilization
- less efficient garbage collection
- more write amplification
decrease the lifetime of SSDs

## Slide 6: Lifetime model

## Slide 7: Markov model
Analyze single SSD’s reliability and device level protection
Page Error Rate Model at x write count
  Bit errors accumulate until access time
  ECC detects / corrects the bit error

## Slide 8: 논문 page 2~3p